History of Weather Modification
Nucleation: Particles + Water Vapor
Number of Aerosols
per unit Volume
1 cm
+
1 cm
1 cm
24 particles / 1 cm3 = 24 cm-3

---
Relative Concentrations
Condensation Nuclei (> 10 nm)
Cloud Condensation Nuclei (CCN)
Ice Nuclei (IN)

---
Condensation Nucleus Counter
Alcohol vapor condenses onto particles which create droplets large enough to be detected one at a time by an optical particle counter. Upon entering the instrument, the air sample passes through a saturation block where alcohol evaporates saturating the flow. The air sample next enters a condenser tube which cools the air sample. Cooling of the air sample creates a supersaturated environment and the alcohol condenses onto particles, regardless of particle composition.

---
Grow Small (>10 nm) Aerosols to Detectable Size
Supersaturated Environment
Undetectable
Particle
Detectable
Particle

---
Cloud Condensation Nuclei (CCN)
Hygroscopic substances such as sodium chloride or ammonium sulfate make good CCN.
Larger particles are generally better CCN than small ones.
Sources
Dust
Smoke
Gas to Particle Conversion

---
CCN Measurement
Expansion Chambers
Gradient Diffusion Chambers
Laminar Flow
Water vapor diffuses from the chamber walls inward more quickly than heat.
The unit operates at a single supersaturation, because the temperature and water vapor gradient along the wetted walls are approximately constant.
The centerline supersaturation depends on the temperature difference between the top and bottom of the column, the flow rate and the absolute pressure in the column.
Xt
Xc
Sample
Flow
Sheath
Flow
Centerline

---
Growth of Droplets
In order to get condensation, the air must be slightly supersaturated with respect to the surface upon which the condensation will occur.
We know what that equilibrium value is if the surface is flat and the water is pure (Clausius-Clapeyron relationship).
Curvature Effect
Water molecules at surface can escape more easily
Solute Effect
r

---
Effect of Curvature
Effect of curvature is to enhance the equilibrium vapor pressure by a factor of 1/r.
Small droplets have a difficult time to keep from evaporating.
This is the primary reason for the fact that large aerosols make better CCN.
r

---
Ice Nuclei (IN)
The freezing process requires a starting point.
Once the starting point is established, the freezing process proceeds rapidly.
The starting point is normally on a solid particle referred to as the “ice nucleus”.
High-speed imaging of ice nucleation in water proves the existence of active sites – See Videos

---
Sources Ice Nuclei
Certain Types of Clay
Certain Bacteria
Nucleation
Homogeneous Nucleation
Heterogeneous Nucleation (Supercooled Droplets)
Similar in concept to supersaturation.
Statistical process.
A supercooled drop will freeze after a long enough time.

---
Effectiveness of Ice Nuclei
Effectiveness is often measured by “threshold temperature”.
Threshold temperature is when one particle in 10,000 will produce an ice crystal.
Different substances have different threshold temperatures ranging from about -5 °C to -40 °C.
Temperature (°C)
Ice Nuclei Concentration (L-1)

---
Activation of Ice Nuclei
Deposition (Sublimation)
Condensation-freezing (Absorption)
Contact Nucleation
Immersion (Bulk Freezing)

---
Concentration of Ice Nuclei
Depends upon temperature, ice nuclei concentrations are commonly measured at -20 °C.
At -20 °C concentrations are often 103 m-3 or lower. (Cloud droplet concentrations are typically of the order of 108 m-3)
Important point in most weather modification programs.
Ice Nuclei Concentration (L-1)
Aerosol Concentration > 0.5 µm (cm3)

---
Relative Concentrations
Condensation Nuclei (> 10 nm)
Cloud Condensation Nuclei (CCN)
Ice Nuclei (IN)