History of Weather Modification
Seeding Equipment & Methods
Based on by Erich Hess

---
Airborne versus Ground Based Seeding
Seeding must be done
At the right place
At the right time
In the right amount
At the best cost

---
Ground Based Cloud Seeding
Benefits
Less costly than aircraft.
Lower maintenance costs.
Fewer people are required.
Disadvantages
Location of generators is very important
Might not be directly in line with storm
Poor dispersal of seeding agent

---
Airborne Cloud Seeding
Benefits
Can place seeding agent in exact location.
Can regulate amount of seeding agent used.
Can provide more complete seeding of a storm.
Disadvantages
More costly.
Greater possibility of down time due to aircraft maintenance.

---
Cloud Top Seeding
Cloud Top Advantages
Good visual Cues
Right Seeding Temperature
Can View Seeding Effects
Faster Nucleation
In-cloud Sampling of updraft, Liquid Water
Cloud Top Disadvantages
No information on cloud base appearance
Top may be embedded
Can’t do at night
May be too turbulent
Seeding agent dispersal not as good

---
Types of Cloud Seeding Tools
Three Types of Tools
Wingtip Generators
Pyrotechnic Devices (Flare Racks)
Chemical Devices (Dry Ice)

---
Lohse Generators
Use ram air pressure for combustion
8 gallons total capacity, 7 usable
Variable flow rate set to 3.2 gph
Used on base seeders in North Dakota

---
Carley Generators
Uses pressurized air for solution flow.
Used when ram air pressure would be too high or too low for Lohse generators.
Must be charged on the ground.
6 gallon capacity.
Variable flow rate is 2.5 gph.

---
Perchlorates Chemical Information
Chemicals in the seeding mixture are strong oxidizers, meaning they can pose a fire hazard.
Contact with the materials should be avoided at all costs.

---
Pyrotechnica Devices Information
Always wear rubber gloves. Clothing that comes in contact with the chemical should be thoroughly washed.
Wear protective goggles.
Store perchlorates in closed containers. Do not drop, skid, or slide containers.
Do not smoke when handling the chemicals.
work with acetone in a well ventilated area.

---
Pyrotechnica Devices Information
Typically use silver iodide (AgI).
2 kinds of flare racks used:
Burn in place
Ejectable
Flares may also contain hygroscopic material (salt).

---
Burn in Place (BIP) Information
Attaches to the back of the wing
Holds twelve 82 gram AgI flares
Burn for just over 2 min.

---
Ejectable Flare Rack Information
Attached to the belly of top-seeder aircraft.
Hold 20 gram AgI flares.
Flares are ignited and then dropped.
The flares should never be dropped below 15,000 ft AGL.

---
Storage and Handling of Flares
Always store flares in the sealed storage containers provided.
Must be stored in a dry area.
Should be treated as an explosive object.
If dropped, inspect for damage. If there is damage, return it.
If one accidentally ignites, remove other flammable objects from nearby.

---
Usage of Dry Ice for Cloud Seeding
Has been used since 1940s
Carried in 150 lb. hoppers in top-seeders
Dry Ice lowers the temperature of the surrounding air to -104° F
This is cold enough to create ice crystals without ice nuclei
As it falls, it promotes the cold rain process

---
Dry Ice Storage and Handling
Lids on storage boxes should be kept tightly sealed, except when needed to get more dry ice.
Should sift pellets through 1/4” hardware cloth to remove any water ice before loading into hoppers.
Have sifted dry ice ready, only load hopper immediately before launch.
Avoid contact with bare skin.

---
Reaction Times of Seeding Agents
Type of Seeding Agent
Time Required for Reaction (min)