History of Weather Modification
Radar for Weather Modification

---
Radio Detection And Ranging (RADAR)
Radar Uses
Military
Weather
Aviation
Traffic Control
(police)
Shipping
Research
Agriculture

---
Weather Detection
Precipitation Measurements
Storm Detection & Tracking
Snow Detection
Cloud Detection
Weather Modification
Wind Measurements

---
Pulsed Radars
Pulsed radars transmit short pulses of energy and wait for returned signals.
Can detect and resolve individual echoes.
Most weather and aircraft radars are pulsed radars.

---
Measurements Conducted with Radar
Distance
Position
Time
Power
Velocity

---
Radar Measurement of Distance
Range - Radar’s Middle Name
Distance = Rate • Time
Distance is “Range”
Rate is speed of light (c)
299,792,458 m/s
6.702 x 108 miles/hr
Time is what radar measures easily and accuracy
https://www.weather.gov/mkx/using-radar

---
Position Radar Measurement Parameters
Range (R)
Azimuth (A)
Requires a horizontally scanning antenna.
Elevation (E)
Requires a vertically scanning antenna.

---
Received Power
(Echo Strength)
Used to calculate radar Reflectivity (Z)
Z is used to estimate Rain Rate (R)
Figure 12 from Baojun Chen, Characteristics of the raindrop size distribution for freezing precipitation observed in Southern China, Journal of Geophysical Research Atmospheres 116(D6), 2011, DOI:10.1029/2010JD015305

---
Velocity Radar Measurements
Obtained by tracking echoes and knowing the time between measurements.
Doppler Shift - Moving targets change the frequency of the returned signal.
Transmit known frequency and measure the frequency shift of returned signal.
Grey line is the transmitted signal. The returned energy changes its wavelength when it hits a target moving away (red line) or toward the radar (green line) https://www.weather.gov/mkx/using-radar

---
Radar Measurements from Aircraft
Must be small, light weight and low power.
Scan ahead of aircraft (±60° or ±90°).
Limited vertical tilt capability.
Size dictates use of short wavelength.
Short wavelength radar is attenuated!
Cannot always see storms through storms.
Used for storm avoidance, not penetration.

---
Block Diagram of Radar
R
A
D
A
R

---
Block Diagram of Radar
Reflector
Antenna
Waveguide
Duplexer
Transmitter
Receiver
Signal Processor
Computer
Display
Master Clock
Modulator

---
Radar Transmitter
Generates the microwave signal.
Transmits a short burst of power at some frequency.
Typical power from a few watts (W) to a couple of megawatts (mW).
UND Radar Transmits 250,000 W or 250 kW.
CPR-HD Radar Transmits 3 mW
Frequency from 30 MHz to 300 GHz
UND / CPR-HD Radars use 5550 MHz = 5.55 GHz

---
WSR 88D Radar Transmitter

---
Transmitter Pulse Parameters
Duration of transmitted pulse is called pulse duration (t) or pulse length (h)
Typically 0.25 µs to 10 µs or longer
1 µs = 10-6 s (~150 m effective length)
Transmitted pulse is repeated many times, called pulse repetition frequency (PRF)
Typically, 150 to 5000 Hz
UND upper limit - 1200 Hz

---
Radar Transmitter Types
Magnetron
Invented in 1939 by the British
Generate power up to 250 kW
Small and light weight
Klystrons
Generate up to 2 MW
Larger/bigger than magnetrons
Very stable frequency output
Solid-state Transmitters

---
Waveguide for Radar
Rectangular Piece of Hollow Waveguide
Flange
Joint
Choke
Joint
Horn
(cross-section)

---
Cross-Section of Parabolic Reflector
Feedhorn
Antenna
Rays from focus are
reflected parallel into space.

---
Radar Reflector Functions
Directs signal into space.
Focuses it.
Generally parabolic in shape.
Larger antennas give smaller beam widths for the same wavelength signal.
Higher frequencies (shorter wavelengths) require smaller antennas for the same beam width.
Aircraft usually use X or C band.
Ground-based radars usually use S or C band.

---
Advantages of using Radar Reflector
Reflectors focus energy into a particular direction.
Reflectors make the energy at some point stronger than it would have been otherwise.
Reflectors allow us to determine direction to a target.

---
Antenna Beam Width
The angular width of an antenna pattern.
The angular width where the power density is one half that on the axis of the beam.
Half-power point, or 3-dB point
Double the angle to get
the half-power point
antenna beam width.

---
Radar Pulse Volume
Pulse Volume
Azimuthal Dimension
Radial Dimension
Main Beam

---
Antenna Sidelobes
There are no perfect antennas!
All antennas have antenna patterns which include:
Main lobe
Side lobes
Back lobes

---
Flat-plate or Phased-array Antenna
More focused beam.
Fewer side lobe losses
Parabolic Antenna
Azimuth Patter
Flat-plate Antenna
Azimuth Patter

---
Principles of Phased Array
https://en.wikipedia.org/wiki/Phased_array

---
Sidelobes During Electronic Scanning
Phased-array Scanning.
There are higher-order main lobes when scan is performed wide range.

---
Radar Receivers
Detect and amplify the tiny signal
received by the antenna
Must be very sensitive.
Typically, radar receivers can detect powers of 0.000 000 000 000 02 W.
This power is more conveniently expressed logarithmically as -107 dBm.
P (dBm) = 10*log10(P (linear power)/1 mW)

---
Radar Receivers Operations
Operate initially at radio frequencies (RF) using low-noise amplifiers.
Signal converted to intermediate frequencies for easier amplification (IF amplifier).
Output is a voltage.

---
A-scope Radar Displays
The original radar display, an oscilloscope.
Time is x-axis, voltage or power is y axis.
Each pulse is shown individually.

---
Plan Position Indicator (PPI) Displays
Map-like display with radar (usually) at center, north to top, east to right.
Range rings give distance.
Intensity shown by brightness (monochrome displays) or color (modern displays).

---
Range-height Indicator (RHI) Displays
Shows a vertical profile along a particular direction (azimuth).
Scans up and down.
Display shows range in x direction and height in y direction.
Intensity shown by brightness or color.

---
Electromagnetic Radiation Characteristics
Wavelength
Frequency
Amplitude
Polarization


---
Radars Transmits at
Microwave Wavelengths
Electromagnetic Spectrum

---
Radar Wavelength Band Types
 Band Designation	Frequency	Wavelength
HF	3-30 MHz	100-10 m
VHF	30-300 MHz	10-1 m
UHF	300-1000 MHz	1-0.3 m
L	1-2 GHz	30-15 cm (20 cm)
S	2-4 GHz	15-8 cm (10 cm)
C	4-8 GHz	8-4 cm (5 cm)
X	8-12 GHz	4-2.5 cm (3 cm)
Ku	12-18 GHz	2.5-1.7 cm
K	18-27 GHz	1.7-1.2 cm
Ka	27-40 GHz	1.2-0.75 cm

---
S and C Band Radar
(10 / 5 cm)
Ground Based Weather Radar
WSR-88D or TDWR

---
X Band Radar
(3 cm)
Airborne Weather
Radar

---
Radar Terminology
Target
Object (or group of objects) that reflect radar energy.
Echo
Reflected radar energy.
Target
Echo

---
Amount of Energy (Echo) Reflected
Size of Targets
Number of Targets
Composition of Targets
Distance to Targets
Echo
Target

---
Size - Bigger Reflects More, ~D6

---
Depends on Composition of Targets
Wet Hail
Rain
Wet Snow
Dry Hail
Dry Snow
Ice Crystals
Most
Reflective
Least
Reflective

---
Depends on Distance to Targets

---
Overall: Radar Reflectivity
Function of amount of energy reflected
Measured in dBZ
Can be considered echo intensity or strength
Related to rainfall rate
Categorized into six levels
Digital Video Integrated Processor (DVIP)

---
Digital Video Integrated Processor (DVIP)
DVIP Level	Rainfall Rate	Reflectivity
1	<.1”/hr	29.5 dBZ
2	.25”/hr	35.9 dBZ
3	.5”/hr	40.7 dBZ
4	1.25”/hr	47.0 dBZ
5	2.5”/hr	51.9 dBZ
6	>4.0”/hr	55.1 dBZ