Experimental Plan to Evaluated Cloud Seeding Materials using Cloud Chambers
David Delene1 and Bruce Boe2
1Department of Atmospheric Sciences, University of North Dakota (UND)
2Weather Modification International, Fargo, North Dakota

---
Experimental Objectives
Use the Pi Cloud Chamber at Michigan Technological University to test Silver Iodide (AgI) cloud seeding flares.
- A flare burning and dilution system is used to produce AgI particles in desired concentrations by burning flares with air flow (70 knots) past the burning flare typical of a seeding aircraft.
- Determine the rate of ice formation after the introduction of an AgI plume into the cloud chamber.
  - Conduct ice formation rate experiments at different temperatures.

---
Experimental Method
- Conduct initial tests using Pi chamber in diffusion mode with liquid water concentrations of 0.5 g/m3 and cloud condensation of 100 #/cm3 and 500 #/cm3 (check for type of ice nuclei activation).
- Measure activation rate (3-5 samples) at temperatures of -4 0C, -6 0C and -10 0C. If time permits, include temperatures of -12 0C and -2 0C.
Process 1 hologram per minute for ~20 minute long experiment.
Test two injection methods.
High (104 #/cm3) AgI Concentration Injection.
Low (102 #/cm3) AgI Concentration Injection.

---
Experimental Setup: Particle Generation System
3.0 inch Diameter, 4.0 ft Long Aluminum Tube
Tank
Tie Down
Strap
Electrical Flare
Ignition Box
Blower Output
(710 ± 200 CFM)
 Air Flow
 1 – 4 minute Burn Duration
(Depends on Flare Length Used)
Blower
Filter Box
70 knots Total Wind
(Similar with Filters)

---
Experimental Setup: Tank Dilution System
Portable Tank Stores AgI Sample for Transfer to Cloud Chamber Lab.
Vacuum
Line
Compressed Air Filter Line
Pressure
Gauge
Inlet
Exit
Tank
(10 Gallons)
Burning
Tube
 CPC
Measure
Particle
Concentration

---
Experimental Setup: Cloud Chamber
Detector
v
Tank
(10 Gallons)

---
Draft Schedule
- Monday Morning:
  - Setup Flare Burning/Dilution System
- Monday ~ 12 – 1 pm:
  - Pick up Bruce from Airport
- Monday 2 or 3 pm
  - Planning Meeting
- Tuesday / Thursday
  - Conduct Experiments
- Friday Morning
  - Review Discussion Meeting.