Update on Cloud Seeding Flare Testing using the Pi Cloud Chamber
David Delene1 and Courtney Steimann1
1Department of Atmospheric Sciences, University of North Dakota (UND)

---
Objective and Overview
Use the Pi Cloud Chamber at Michigan Technological University to test Silver Iodide (AgI) cloud seeding flares.
- A flare burning and dilution system is used to ensure that the Pi Cloud Chamber is not contaminated by AgI
- The system burns flares reproducing the air flow over flares at aircraft speeds and provides particle dilution of between 105 and 106 in number concentration.
- Test the burning and dilution system to determine particles size and concentration.

---
Lab Building Roof
Fume Hood Blower (710 ± 200 CFM)
 SMPS
Dilution
CCNC
CPC
Air Flow into
Fume Hood
and out Top
of Building
3.0 inch Diameter, 4.0 ft Long
Aluminum Flare Burning Tube
3.0 inch Diameter, 4.0 ft Long
Aluminum Flare Burning Tube
Sampling
Ports
Variable
Speed
Blowers
Joint
 Air
Flow
Electrical Flare
Ignition Box
75 Knots Flow Rate
`

---
Burning and Dilution Setup
First Version
Valve
Dilution
System
Tie Down Strap
Electrical Flare
Ignition Box
Filter Box
Reduced Flow Rate, Even with Large Filter
15,000 #/cm3 Total Particle Concentration
Blowers

---
Value Dilution System Results: 2017/12/05
105
Value 1 Dilution
Value 2 Dilution
104
103
Value 1 & 2 Dilution
102
16:30
17:00
17:30
Time (UTC)
Concentration (#/cm3)

---
Burning and Dilution Setup
Current Version: April 2018
Tie Down Strap
Electrical Flare
Ignition Box
Filter Box
Blower
47 knots Total Wind
(Similar with Filters)

---
Tank Dilution System
- Initial Testing is done using a 10 gallon tank.
- A one milliliter air sample is obtained using glass syringe.
- The syringe transfers sample from flare burning system to tank.
- Tank diluted samples will be compared to valve system using CPC and SMPS to measure concentration and size distribution.

---
Legend
        Condensation Particle Counter (CPC)
        Needle Injection System
        Air Flow Direction
Vaccuum
Line
Compressed Air Filter Line
Pressure
Gauge
Inlet
Tank
Burning
Tube
 CPC

---
Calculated Dilution Ratios
Tank Size (Galloons)
Dilution Ratio
Size (Gallons)	Ratio
10	3.84
30	1.15
60	2.35
100	3.85

---
Summary and Conclusions
- Final Check on Tank System to ensure no contamination and burning and dilution system is ready for deployment at Pi Cloud Chamber.
- The Holodeck instrument is installed in the Pi Cloud Chamber
- Two periods of setting at the Pi
  Cloud Chamber are planned for
  this summer.

---
Questions and Discussion