## Slide 1: Visibility Comparison of the Unmanned Aircraft System Deployable MiniOFS to a Present Weather Sensor
Isaiah Nault

## Slide 2: Introduction
Problem: fog is a hazard to aircraft > causes poor visibility
  Small aircraft are impacted more due to lower flying patterns (Leung et al, 2020)
Purpose: Compare a UAS deployable sensor to a ground based present weather sensor
  Research and data analysis of a fog event in the Grand Forks area
  This research will help determine if the Miniofs is reliable for deployment on UAS
UND Mettrailer Deeplens Camera 2: 1505 UTC
UND Mettrailer Deeplens Camera 2: 1435 UTC

## Slide 3: Introduction
Fog is commonly formed when moist air is cooled - after rain events - early morning
Visibility threshold causing danger - 800 m (Leung et al. 2020)
October 4th, 2010 - 96 people died in Smolensk, Russia - President of Poland
Improper soundings available at the time led to the crash (Cosmin-Liviu et al. 2021)
UAS can take readings anywhere in the fog
Easily deployable, no human factors, can fly lower

## Slide 4: CS-125 Present Weather Sensor
Calculates average every minute & reports
Can identify precipitation type
Uses forward scatter method at 42 degrees
Readings from 0.005 km to 75 km
Weighs 4 kg with mounting plate
(Campbell Scientific, 2013)

## Slide 5: Forward Scatter Method
Forward Scatter Method: light is scattered in a forward direction
  Collides with particles scattering light in all directions > peak scatter angle is 42 degrees > more sensitive
  The sensor uses a receiver to collect the light
  Uses IR with a wavelength of 850 nm
(Campbell Science, 2013)
(Azzawi et al. 2016)

## Slide 6: CS-125 Precipitation Detection
Uses algorithms to determine precipitation type
Uses the amplitude of the signal received as a guide to the particle size and speed as it represents the time taken to fall through the scan area
The CS-125 also has a temperature sensor
The figure shows how these outputs are used to determine precipitation type
The UAS deployable sensor does not have this ability

## Slide 7: MiniOFS Deployable Sensor
Ideal for use on UAS
  - Calculates the average over 30 seconds & reports
  Weighs only 0.17 kg
  Cheaper
Visibility range of 0.02 km - 4 km
Uses 180-degree back scatter method - 0.25 m ahead of sensor
(Optical Sensors, 2013)

## Slide 8: Backscatter Method
Back scatter method: light is scattered in the backward direction and received by a sensor
  Uses a 3 mW IR led with a wavelength of 850 nm
  Much more compact
  Severely underestimate visibility in snow > false scattering
  Less light is scattered at 180 degrees than 42 > not as sensitive
(Azzawi et al. 2016)

## Slide 9: Flight Rating Requirements
Grand Forks International Airport is a Class D airspace
(FAA, 2022)

## Slide 10: Methodology
Radiation fog event - 28 August 2021 0.2 km visibility
Data was downloaded from CHORDS-UND database

## Slide 11: Methodology
Mean, and standard deviation was calculated from different periods in the event to compare the MiniOFS to the CS-125
  - Periods include the start of low visibility period, Lowest visibility period, and the spike in visibility period
Mean used to determine agreeance over a given period
Standard deviation to determine variance

## Slide 12: Methodology
V: Average visibility over a one-minute period
X1: Visibility reading at the beginning of a one-minute period
Y: Number of seconds past the minute that the first visibility reading was taken
X2: Second visibility reading at the end of the one-minute period

## Slide 13: Methodology
Standard Deviation
Population Average
Number of Data Points
Iterated Value From the Population

## Slide 14
MiniOFS: 1957 +/- 1017
CS-125: 2132 +/- 1778
Mean Difference: 175 m MiniOFS under CS-125 by 8.2%​
Start of Low Visibility

## Slide 15
MiniOFS: 290 +/- 87
CS-125: 300 +/- 59
Mean Difference: 10 m MiniOFS under CS-125 by 3.3%​
Lowest Visibility

## Slide 16
MiniOFS: 2282 +/- 636
CS-125: 2185 +/- 663
Mean Difference: 97 m MiniOFS over CS-125 by 4.3%
Spike in Visibility

## Slide 17: Study Comparison
248 datapoints from 0649 UTC - 1056 UTC
MiniOFS is known to overestimate visibilities under 1km in comparison to the Vaisala PWD-11 sensor (Michna et al. 2007)
This study showed a better result in comparison > different sensors > calibration
(Michna et al. 2007)

## Slide 18: Conclusion
MiniOFS did not overestimate greatly under 1km in comparison to the CS-125 > better result than with the PWD-11 sensor used for the Michna et al. study
Areas of consideration for the MiniOFS:
  More scattered readings while visibility is rapidly changing
  Records only up to 4 km visibility > VFR/IFR covered
  Lightweight, small, and affordable > ideal for FAA regulations

## Slide 19: Conclusion
Over 513 data points from 0618 UTC - 1459 UTC
  MiniOFS overestimated by 74 m on average which is a 9.9% increase compared to the CS-125 mean of 751 m
This error is relatively small if in use for low visibility purposes
Use of the MiniOFS can build the foundation for better atmospheric picture

## Slide 20: Conclusion
Additional Research:
Accuracy of the MiniOFS while deployed on UAS due to rotor wake
Comparison of MiniOFS & CS-125 under different visibility restricting events such as smoke, and haze
Accuracy of MiniOFS after calibrating the MiniOFS and one other sensor > Michna et al. did not mention a calibration

## Slide 21: References
Available per request