Introduction
March 15, 2007
David Delene
delene@aero.und.edu
http://aerosol.atmos.und.edu
[Speaker Notes: Lecture prepared by David Delene for UND 2007 Air pollution workshop.]

---
Title
Atmospheric Particle
Concentration Measurements: Surface, Aircraft and Balloon Platforms

---
Satellite
Importance of Aerosols
Satellite image of Asian dust storm and air pollution (April 2001).
[Speaker Notes: Image taken from http://www.esrl.noaa.gov/gmd/about/airquality.html.]

---
Definitions
Definitions
Aerosols
Suspended solid or liquid matter
Small settling velocity
Atmospheric Aerosols
Suspended material in the Earth's atmosphere that have residence times of days, to a few weeks.
Atmospheric Aerosols are sometimes referred to as “particles”

---
Size
Atmospheric Aerosol Size Range
10-9m to 10-5 m
(.001 µm to 10 µm or 1 nm to 10,000 nm)
Wavelength of Visible Light?
Size of a human hair?
 1
.0001
.01
.0001
.001
.01
..1
.001

---
Concentration
Aerosol Number Concentration
Number of Aerosols per unit Volume
1 cm
1 cm
1 cm
24 particles / 1 cm3 = 24 cm-3

---
Grow
Grow Small Aerosols
to Detectable Size
Supersaturated Environment
Undetectable
Particle
Detectable
Particle

---
Diffusion
Thermal Diffusion Chamber
T2
T1
Top Plate Warm & Moist (T2)
Bottom Plate Cold & Moist (T1)
Temperature and Water Vapor Gradients Between Plates

---
Scattering
Light Scattering and Absorption by Aerosols
Volume of Air
In Coming Light
Out Going Light

---
Instruments
Aerosol Instruments
[Speaker Notes: The University of Wyoming balloon-borne CCN Counter. The other images are from TSI, A 3010 CPC, 3025 ultrafine counter, and a 3080 Electrostatic Classifiers (www.tsi.com).]

---
Surface
Surface Sites
 Bondville, Illinois Lamont, Oklahoma Barrow, Alaska

---
MLO
Mauna Loa Observatory

---
System
New Aerosol System

---
Dust
Dust Event at Mauna Loa
(April 2000)

---
MLO Data
Seasonal Data at Mauna Loa
(1974-2003)
Jan Mar May Jul Sep Nov Ann
Scattering Coefficient [Mm-1]

---
172XP
Aircraft Aerosol System
Aerosol Inlet
Cessna-172XP
The inlet is mounted on the starboard (right) wing of the aircraft.
The inlet nozzle is a diffuser designed with slightly rounded leading edges.
The nozzle orifice was sized to be isokinetic for typical C172 airspeeds (~50 m/s)
The nozzle and inlet tube are constructed of anodized aluminium
Large diameter conductive tubing passes aerosols to the instruments.

---
Rack
Aircraft Aerosol System
Front (Starboard) View of Rack
View of Rack from Rear of Plane
Back (port) View of Rack
The aerosol instrumentation payload is bolted down inside the Cessna.
Instruments rack consists primarily of a TSI nephelometer and a particle light absorption photometer.

---
Profile
Aircraft Profile Summary above Lamont, Oklahoma
Light Extinction [Mm-1]
Altitude [m]

---
Crystal-FACE
Crystal-FACE Research Aircraft
ER-2
Proteus
WB-57
Citation
P-3
Twin Otter
Crystal-FACE is a measurement campaign designed to investigate tropical cirrus cloud physical properties and formation processes.
Understanding the production of upper tropospheric cirrus clouds is essential for the successful modeling of the Earth's climate.

---
FMPS
Fast Mobility Particle Sizer Measurement Features
Particle measurements between 5.6 to 560 nm in 32 channels.
Particle size distributions with one-second resolution.
Particle concentration range across more than 4 orders of magnitude.
Self contained and runs on 120 volts AC power.
Data collection and analysis software.

---
FMPS Install
Installation of the FMPS in the UND Citation Research Aircraft
Exterior of the Inlet and Outlet use for FSMP on the UND Citation Aircraft.
Interior of the Inlet and Outlet use for FSMP on the UND Citation Aircraft.
The Fast Mobility Particle Sizer in a rear rack on the University of North Dakota’s (UND) Citation Research Aircraft.

---
FMPS Spectrum
FMPS Measured Size Spectrum on September 2, 2005 in Grand Forks
Exterior of the Inlet and Outlet use for FSMP on the UND Citation Aircraft.
Interior of the Inlet and Outlet use for FSMP on the UND Citation Aircraft.
The Fast Mobility Particle Sizer in a rear rack on the University of North Dakota’s (UND) Citation Research Aircraft.

---
New Zealand
New Zealand Balloon Launch

---
Filling
Filling Balloon for Launch

---
CCN Counter
University of Wyoming Balloon-borne Cloud Condensation Nucleus Counter
[Speaker Notes: Picture of University of Wyoming Balloon-borne CCN counter, from around 1997.]

---
Ballong Profiles
Balloon-borne Aerosol Profiles
[Speaker Notes: Picture of University of Wyoming Balloon-borne CCN counter, from around 1997.]

---
Summary
Summary
Aerosols are suspended particles in the atmosphere that affect the scattering and absorption of sunlight and affect cloud and participation process.
To understand atmospheric aerosols require measurements from surface, aircraft and balloon platforms.
Conducting measurements to learn about the atmosphere can be a lot of fun!
[Speaker Notes: Things students should be able to do.]

---
Questions
     Any Questions?

---
Importance
Importance of Aerosols
Direct Forcing
Indirect Forcing
Carbon Dioxide Forcing
Total Forcing
Climate forcing predicted from the Lawrence Livermore National Laboratory Global Aerosol Model [Catherine C. Chuang and Joyce E. Penner].
[Speaker Notes: Model very old, from around 1994.]

---
Diagram
 Passive Cavity Aerosol Spectrometer Probe
[Speaker Notes: From http://raf.atd.ucar.edu/~darrel/htmlFiles/pcasp100.html]

---
OPC
Optical Particle Counter
Operating Principles
Detects single particles and sizes them by measuring the intensity of light that the particle scatters when passing through a light beam.
The light beam can be either from a white light source or a laser.
The size of the particle is determined by measuring the light scattering intensity and using Mie scattering theory to relate this intensity to the particle size.
[Speaker Notes: Top Picture: LASAIR aerosol particle counters are known for their high reliability, long life and minimal maintenance requirements. The LASAIR is offered in a variety of models providing a wide range of flow rates and sizing channels. From - http://www.pmeasuring.com/particle/products/aerosol Passive Cavity Aerosol Spectrometer Probe Images is from http://raf.atd.ucar.edu/~darrel/htmlFiles/pcasp100.html]

---
PSAP
Particle Soot Absorption Photometer
Beers Law
A=ln(IO / I)
A is the absorbance
I is the intensity of light transmitted
Io is the light intensity before passing through the filter.
Quartz Filter
Reference Signal
Attenuated Signal
Particle Deposit
Green LED
Opal Glass
O-Rings
Detectors
Filter Holder

---
Nephelometer
Integrating Nephelometer
TSI 3563 Nephelometer schematic courtesy of TSI Incorporated
     Beer-Lambert Law
       I / Io = e (- Ã x)
Io = intensity of light source
I = intensity of light after passing through atmospheric path
x = thickness of medium through which light passes
Ã = total extinction coefficient (scattering + absorption)

---
Measurements
Instrumentation Based Aerosol Definitions
Ultrafine Aerosols (UF)	Aerosols larger than 3 nm diameter.
Condensation Nuclei (CN)
Aerosols larger than 10 nm diameter.
Optical Aerosols (D0.3)	Aerosols larger than 0.3 m diameter.
Cloud Condensation Nuclei (CCN)	Nuclei on which cloud droplets form.
Ice Nuclei (IN)	Nuclei on which ice crystals form.

---
CN Counter
Condensation Nucleus Counter
Alcohol vapor condenses onto particles which create droplets large enough to be detected one at a time by an optical particle counter. Upon entering the instrument, the air sample passes through a saturation block where alcohol evaporates saturating the flow. The air sample next enters a condenser tube which cools the air sample. Cooling of the air sample creates a supersaturated environment and the alcohol condenses onto particles, regardless of particle composition.

---
Vapor Pressure
Vapor Pressure
Ambient vapor pressure is linear from top to bottom.
Saturation vapor pressure is a curve from top to bottom.
A supersaturation exists between top and bottom
[Speaker Notes: From David Delene Disseration Work.]

---
Beers Law
Particle Soot Absorption Photometer
Beers Law
A=ln(IO / I)
A is the absorbance
I is the intensity of light transmitted
Io is the light intensity before passing through the filter.
Absorption coefficient is given by:
 bap = (area/volume)*ln(Io/I)
bap is the absorption coefficient [m-1]
Area is the area of the sample spot [m2]
Volume is the volume of air sampled in averaging period [m3]
I is the average filter transmittance for averaging period
Io is the average filter transmittance for averaging period

---
Filter
Particle Soot Absorption Photometer
Principle of operation is to measure the change in light transmission through a filter on which particles are collected.
Calibration uses a reference absorption determined as the difference between light extinction and light scattering.
Instrument exhibits a significant response to nonabsorbing aerosols and overestimates absorption due to suspended particles by about 20-30%.
Quartz Filter
Reference Signal
Attenuated Signal
Particle Deposit
Green LED
Opal Glass
O-Rings
Detectors
Filter Holder

---
Neph Diagram
Integrating Nephelometer
TSI 3563 Nephelometer schematic courtesy of TSI Incorporated
The Nephelometer detects aerosol scattering by measuring total light scattered and subtracting light scattered by the air, the instrument walls and the detector background noise.
Calibration is done by measuring two reference gases with know scattering values, typically air and CO2.
The nephelometer measures from 7-170o scatting angles and the backsctter shutter allows blocking of angles from 7-90o. Measurements are corrected to the 0-180o and 0-90o range.

---
SGP Profile
Aircraft Profile Summary

---
Wing Probes
Wing Mounted Instruments

---
Temp/RH
Aircraft Aerosol System
Temperature and Relative Humidity Sensor
The temperature/Relative Humidity sensor (Humicap, Vaisala Inc.)
is mounted on the outside of the aircraft on the the bottom of the right
(starboard) wing. The sensor is mounted inside a counter-flow inlet